## Slide 1: The Digital Downconverter
Rodney Staggers Jr
Ph.D. Student
Arizona State University

## Slide 2: Description
This assignment explored how radio signals are processed, using a local oscillator mixer, low-pass filter, and downsampling, to isolate desired frequencies.

## Slide 3: Digital Downconverter System Block Design

## Slide 4: Incoming Frequencies
We chose a sample rate of 500MHz, and had data come in at 10,37, & 85MHz.
  Thus satisfying the Nyquist requirement of being at least twice the bandwidth.
To simulate the noisiness of real incoming signals, Additive White Gaussian Noise was added.

## Slide 5: Mixing Stage
Our Magical frequency was 10MHz. After adding the 10MHz local oscillator, which is modelled as , frequencies are produced at 0 and 20MHz.
When Mixing, we multiply the incoming signal with the one shown above.

## Slide 6: Mixing Stage
The incoming signal:
  Where
Using the trig identity:
We find that for our magic frequency of 10MHz, which is modelled as (), the mixing gives the following function:

## Slide 7: Low Pass Filter and Downsample
After going through the LO-mixer, we apply a 2MHz low-pass filter to remove everything above that. Since the baseband difference frequency for our magical frequency was 0MHz, and all other frequencies range from 10-95MHz, this will leave just one lone tone.

## Slide 8: Low Pass Filter and Downsample
We subsequently apply a downsample of 50, reduces the original bandwidth to 2MHz and the new sample rate to 10MHz.

## Slide 9: What I learned
The exploration process enhanced my repertoire in filtering out noisy datasets to isolate areas of interest, while also saving computational costs.